## Slide 1: Signage for the Cal Poly Dairy Parlor
Kevin Mohan
3/01/13

## Slide 2
WARNING: Crowd gate will continue moving backwards unless set to FORWARD setting.
WARNING: Do not drop the crowd gate until sure that all cattle and workers are clear.

## Slide 3
Advisory: Remember to seal the line before beginning milking or wash cycles.

## Slide 4
Advisory: Remember to remove the milk feed pipe from the tank upon completion of milking.

## Slide 5
Advisory: Insert float balls before milking.

## Slide 6
Advisory: Flow direction levers go down while milking and up during the wash cycle.

## Slide 7
1. Dip: Pre-dip all four teats, making sure to cover at least 2/3 of the way up each teat. Allow dip at least 10 seconds exposure before stripping
2. Strip: Strip 3 full strips of milk out of each teat. Check to see that milk is clear of chunks or flakes from mastitis.
3. Wipe: Wipe each teat clean of debris and dirt. Use a separate towel for the udder of each cow.
Note When Milking

## Slide 8
4. Attach: Put the machine on the cow, with the chain attachment facing her front and the hose attachment facing her rear. Make sure no air is squawking through the teat cups and that all attachments are tight.
5. Check: Once the machine has finished milking and retracted, check the cow to see if she has been sufficiently milked out. Check that her udders are not engorged with milk. When in doubt strip a few test strips to be sure.
6. Dip: Post-dip the cow to prevent potential infection. Make sure to cover 2/3 of the way up the teat, and ensure full coverage of the teat end.

## Slide 9
Wash: When using the CIP system, make sure that the CIP hose is attached with gasket in place and the handle on the left hand side of the attachment point is flipped downward.
Drain: When draining the filters and milk lines, unscrew the ring clip on the CIP attachment point and remove the cap. The handle on the left hand side should be in the downward position.
Milk: When milking, the cap should be in place on the bottom of the CIP attachment point and sealed with a ring clamp, while the handle on the left hand side should be in the upward position.
CIP Attachment Settings