## Slide 1
Storyboard
Availability: source, sinks and measurements
Fresh water quality: Green, blue and grey water
Example: the connection between energy use and water use
Water footprints depend on cultural practices rather than human necessities
Using Meadow’s hierarchy of systems interventions reveals high-leveraged opportunities
Expanding IPAT equation reveals high-leverage design opportunities
Stocks:
The water footprint
Sources and sinks: the water cycle
Awareness of facts:
Fresh water resources differ in quality and availability
Main point
Fresh water resources are critical to all life forms and therefore its use should be minimized in designs
Awareness of strategies:
Human practices can shift toward less impactful & restoring alternatives
Awareness of personal role:
High leverage interventions involve shifts in human behavior
Flows: Global consumption
Water
This work was made possible in part by the National Science Foundation Grant DUE#0717428 | Jane Qiong Zhang and Linda Vanasupa

## Slide 2
An Introduction to Water
2
Notes: 2

## Slide 3: Global water picture
System Boundary
Conceptually “separates” the system and surroundings
A closed thermodynamic system
3
E
Can exchange energy but not enough mass to affect its thermodynamic state
Classroom Activity (5 minutes)
In a closed thermodynamic system, is the amount of fresh water available variable or fixed?
Notes: This image depicts the earth as a (conceptual) system with a system boundary. In effect, the earth is a closed thermodynamic system. This means it can exchange energy with its surroundings but not enough mass to affect its thermodynamic state. Some may say, “what about satellites that we launch into outer space?” True, that is removing mass from the earth, but this is not enough mass to change the thermodynamic state (temperature, pressure or volume) of the earth itself.
The consequence of the earth being essentially a closed system is that all that is needed for life must be produced on earth from the things that are already on earth (i.e., from the mass that is already here) and all the is produced in the form of waste must either be absorbed on earth or accumulated on earth.
Activity:
From this activity, people will likely be able to determine that they would need to know how much each person consumed per year and how much the earth produced for consumption. This activity should begin revealing the influence of “life style” choices on the limit, or “carrying capacity” of the earth. The thing that they may not get is that they would also need to know how much waste is produced per year and how much waste the earth can “absorb” per year. These are a consequence of the earth being a closed system.
It is very important to acknowledge that this problem is considering balancing consumption RATE, production RATE, absorption RATE (wastes). That is, it is a problem about flows in the same way that an interest-earning bank account is about flows of interests into the primary account. A common question is around “How much resource use is too much?” In other words, we have a primary bank account of resources and how much can we “spend” before we are globally, irreversibly out of balance? In a way,
Learning Objectives: 1.1, 1.2, 1.7

## Slide 4: The global water picture: do we have enough?
96.5% ocean
2.5% fresh water
0.1 % in air
Classroom Activity
(5-10 minutes)
Turn to your neighbor and determine what you’d need to know in order to answer the question, “Is this enough water?”
Global water stock ~1.4 x 109 km3
Notes: Well, not all water is alike. Let’s consider the nature of the water that is on the planet. If we were to put all the available water in a container, it is estimated that the volume is about 1.4 billion cubic km.
About 2.5% of this amount is in the form of freshwater from lakes, rivers and streams.
If we are attempting to answer the question, “Is this enough water?” What would we need to know?
Notes: This is a complex question. There is no “correct” answer, but in attempting to consider how you’d go about answering the question, you would have to notice the difference between salt water and fresh water. What is usable to us as humans? Who and what would be included in the calculations (e.g., Would plants and animals be included? Do you consider human life to be dependent upon healthy ecosystems?)
A simplistic answer would reflect only a quantitative computation of human water use. If one ONLY considered human economic activity, you can compute the global use from the values given in the paper A. Y. Hoekstra and M. M. Mekennon, “The water footprint of humanity.” PNAS, Feb. 28, 2012, vol. 109, no. 9, www.pnas.org/cgi/doi/10.1073/pnas.1109936109.
This amount of water is about 9K cubic km/year. This water estimate includes the amount of freshwater needed to dilute polluted water to the “acceptable” level of pollutants, without regard to type of pollutant. That is, it is a quantitative measure that gives a proxy indicator of water quality as that total concentration of pollutants. This measure leaves out a great deal. It is also not a direct measure of water use, but of estimated water consumption based on a set of criteria for diluting polluted water and historical methods for agricultural practices. The primary values in the computations include water “consumption” and estimated consumption through industrial activities.
Also note that these estimates do not address anything about what is necessary. They are based on estimates of the historical activities and water use n the HUMAN economic systems. They do not include uses of water by other living organisms. Students thinking in a more sophisticated way will begin to ask questions about the computations and whether other organisms are considered. They may ask questions about replenish rates and how “fresh water” stocks are replenished.
A very sophisticated set of questions will be around human value systems and whether we should consider only human values or incorporate needs of nature. Questions will consider also the distribution and availability of fresh water.
Data source: See page 358, J.R. Mihelcic and J.B. Zimmerman (Environmental Engineering: Fundamentals, Sustainability, Design, John Wiley & Sons, Inc., 2010) for more information.
Learning objectives: 1.7, 5.1

## Slide 5: Fresh water scarcity
“Almost half the world’s population face a scarcity of water.”
The Millennium Development Goals Report 2008,
The United Nations
Goal 7: Ensure Environmental Sustainability
  Target 3: Halve, by 2015, the proportion of the population without sustainable access to safe drinking water and basic sanitation
Classroom Activity (5-10 minutes)
If engineered products, goods and services cause water shortages and subsequent risks to human welfare in a remote part of the globe, is this of a concern to engineers? Why or why not?
Notes: Learning objectives: 3.1, 3.2, 4.1, 5.1, 5.2, 5.3

## Slide 6: Quality measures of water
Notes: This graphic summarizes the water quality measures (on the left) and the major constituents found in natural water.
Details on the major constituents:
Major inorganics: Calcium (Ca2+), chloride (Cl-), fluoride (F-), iron (Fe2+), manganese (Mn2+), nitrate (NO3-), sodium (Na+), sulfur (SO4 2-, HS-)
Minor inorganics: Cadmium, chromium, copper, lead, mercury, nickel, zinc, arsenic
Naturally occurring organic compounds: naturally occurring organic matter (NOM) that is measured as total organic carbon (TOC)
Anthropogenic organics: synthetic organic chemicals (SOCs) and emerging chemicals of concern used in industry, households, and agriculture (e.g., benzyne, methyl tert-butyl ether, tetra-chloroethylene, trichloroethylene, vinyl chloride, alachlor)
Details on the water quality measures.
Turbidity is the measurement of optical clarity of water and is caused by suspended particles in water. It is measured with a turbidimeter and reported in nephelometric turbidity units (NTU).
Particles found in water that are important to water treatment range in size of 0.001-100 μm. The different particles are characterized as: 1) suspended solids (particles larger than 1 μm), 2) colloidal particles (between 0.001 and 1 μm), and 3) dissolved particles (smaller than 0.001 μm).
Color in water is caused by natural organic ions, turbidity, and dissolved organic matter.
Taste and odor can result from natural inorganic and organic constituents and biological sources being dissolved in water, and can also result as an outcome of water treatment.
Temperature of both groundwater and surface water can vary depending on seasons, location, and depth.
The above information is from Tables 10.1 Concentration of Major Constituents Found in Water, page 398, and 10.2: Physical Characteristics of Natural Water can be found on page 399, J.R. Mihelcic and J.B. Zimmerman (Environmental Engineering: Fundamentals, Sustainability, Design, John Wiley & Sons, Inc., 2010).
The table summarized the different physical characteristics of natural water (same as untreated or raw water), such as turbidity, particles, color, taste and odor, and temperature. For further explanations of the physical characteristics, please see pages 398-400.
Learning Goals: 1.3, 1.4, 1.5, 1.6, 6.1, 6.2

## Slide 7: Lacking improved water supply and sanitation
Notes: Table 1.3: Distribution of Global Population Not Served with Improved Water Supply and Sanitation
Table is from page 11, J.R. Mihelcic and J.B. Zimmerman (Environmental Engineering: Fundamentals, Sustainability, Design, John Wiley & Sons, Inc., 2010).
This figure shows the populations, by region, that are lacking improved water supply and sanitation. Europe is not shown. Four % of the population in Europe lacks improved water supply, 8% of the population lacks improved sanitation. The United States and Canada are not listed on this figure, as coverage approaches 100% for these two countries. It can be seen that there is a greater percentage of the population that still lacks access to improved sanitation (2.5 billion people lack access to any type of sanitation equipment) than compared to the global population that lack access to improved water supply (900 million people lack access to an improved water supply). However, it can be seen that major improvements still need to be made if we want to decrease the percentage of the global population that is not served with improved water supply and sanitation.
In addition, it is important to understand the health impact on not having access to an improved water source and lack of access to improved sanitation. Pathogens, disease causing agents, can be transmitted through contact with water, air, and solid waste. Environmental engineers need to understand the importance of protecting the public’s health when providing a population with a sustainable appropriate technology.
Learning Goals: 1.6, 2.1, 3.3

## Slide 8: Number of months when blue water footprint > availability
Classroom Activity (5-10 minutes)
What would it mean to if the people in a region to have a blue water footprint that is larger that what is available through rivers and groundwater?
Hoekstra AY, Mekonnen MM, Chapagain AK, Mathews RE, et al. (2012) Global Monthly Water Scarcity: Blue Water Footprints versus Blue Water Availability. PLoS ONE 7(2): e32688. doi:10.1371/journal.pone.0032688
http://www.plosone.org/article/info:doi/10.1371/journal.pone.0032688
Notes: This graphic depicts the regions throughout the world where the amount of water needed to sustain human life and dilute pollutants to “acceptable levels” exceeds what is available through rivers and groundwater.
The question revels the “dilemma” of the “water footprint” tool. The computation includes how much water is needed to dilute toxins to “acceptable levels”.
According to the article, agriculture accounts for 92% of the global blue water footprint. The remainder is shared equally between industrial and residential use.
Figure reference: Hoekstra, A.Y., Mekonnen, M.M., Chapagain, A.K., Mathews, R.E. and Richter, B.D. (2012) Global monthly water scarcity: Blue water footprints versus blue water availability, PLoS ONE 7(2): e32688.
Learning Goals: 3.3, 5.2

## Slide 9
Water stocks and flows
9
Notes: 9

## Slide 10: Hydrologic Cycle
J.R. Mihelcic and J.B. Zimmerman (Environmental Engineering: Fundamentals, Sustainability, Design, John Wiley & Sons, Inc., 2010).
Notes: Figure 9.1: The Hydrologic Cycle -Units of water transfer are 1012 m3 / yr
The hydrologic cycle consists of the pathways for how water moves and is distributed on the planet.
The quantity and quality of water varies greatly as it moves through the cycle.
-Groundwater systems can extend from Earth’s surface to meters to kilometers below the surface.
-These systems are typically composed of porous solid materials (i.e. sand, gravel, and clay) containing water and air.
-Solid and fractured rock also can be thought of as porous materials that compose groundwater systems.
The following web link (http://www.fwee.org/hlogic.html) provides a detailed, but simplistic explanation of the hydrologic cycle (The water cycle).
Figure is from page 355, J.R. Mihelcic and J.B. Zimmerman (Environmental Engineering: Fundamentals, Sustainability, Design, John Wiley & Sons, Inc., 2010). Used with permission.
Learning Goals: 1.1, 2.4, 2.5, 2.6, 6.2

## Slide 11: Water Resources
Surface water
groundwater
Reclaimed water
precipitation
Classroom Activity (5-10 minutes)
Do you consider the ocean a water resource? Why or why not?
Notes: Definitions:
Ground Water All subsurface water that fills the pores, voids, fractures, and other spaces between soil particles and in rock strata in the saturated zone of geologic formations (from http://ohioline.osu.edu/aex-fact/0460.html).
Surface Water The water from all sources that occurs on the Earth's surface either as diffused water or as water in natural channels, artificial channels, or other surface water bodies (from http://ohioline.osu.edu/aex-fact/0460.html).
Precipitation The process by which water vapor condenses in the atmosphere or onto a land surface in the form of rain, hail, sleet or snow (from http://ohioline.osu.edu/aex-fact/0460.html).
Reclaimed Water the “effluent derived in any part from sewage from a wastewater
treatment system that has been adequately and reliably treated, so that as a result of
that treatment, it is suitable for a beneficial use or a controlled use that would not
otherwise occur and is no longer considered wastewater (from http://www.ecy.wa.gov/Programs/wq/reclaim/DraftRWDef.pdf).”
Each of these water sources can be further analyzed for their microbial and chemical quality as well as seasonality.
Surface water has poor microbial quality and varied chemical quality as it is dependent on any agricultural runoff and upstream human uses. Regarding seasonality, the surface water source could dry up during the dry season, where as in the rainy season increased runoff could increase the pathogen and chemical load in the surface water.
Groundwater has good microbial quality unless it is near a latrine, or waste dumping site. The chemical quality will vary depending on personal preference and may contain issues of hardness and other dissolved metals. Localized issues of high arsenic and fluoride concentrations can be found in some groundwater based on geographic location. During the dry season, shallow water tables could be affected and decline, whereas deeper wells may continue to produce sufficient quantities of water despite the season.
Rainwater’s microbial quality can be very poor before a first flush is carried out, and then varies depending on the roofing material. The chemical quality of rainwater is typically good, and the seasonality can affect availability of rainwater. During the rainy season there should be plentiful quantities, and the rainwater can be stored for later use during the dry season.
Reclaimed water or greywater has poor microbial quality as it can be contaminated with fecal coliforms and other pathogens. Regarding the chemical quality, it tends to be high in suspended solids, and possibly high in phosphorus depending on types of soaps used. The seasonality will affect the amount of greywater based on the availability of other water sources.
The above information regarding microbial and chemical water quality and seasonality can be found in Table 9-7 on page 172 of Mihelcic, J. R., Fry, L.M., Myre, E.A, Phillips, L.D., & Barkdoll, B.D. (Field Guide to Environmental Engineering for Development Workers: Water, Sanitation, and Indoor Air, ASCE Press, 2009).
Learning Goals: 1.2

## Slide 12: Freshwater Availability
Chart: Percent of World's Total Freshwater in Different Locations
| Glaciers and Permanent Snow Cover | Groundwater | Other Freshwater Sources
World Freshwater Sources | 68.7 | 30.1 | 0.389
Chart: Percent Composition of World's Other Freshwater Sources
| Lakes | Soil Moisture | Atmosphere | Marshes and Swamps | Biological Water | Rivers
 | 0.26 | 0.05 | 0.04 | 0.03 | 0.003 | 0.006
Classroom Activity (5-10 minutes)
Some companies want to harvest glaciers to sell for fresh water. Do you consider this a good idea? Why or why not?
Notes: This figure was developed from the information found in Table 9.1:Percent of World’s Total Freshwater in Different Locations, on page 358, J.R. Mihelcic and J.B. Zimmerman (Environmental Engineering: Fundamentals, Sustainability, Design, John Wiley & Sons, Inc., 2010). Also refer to this page for further information on freshwater availability.
Furthermore,
-Only 2.5% f the world’s total water budget is estimated to be freshwater.
-70% of this 2.5% is in the form of glaciers and ice sheets.
-A large percentage of the world’s freshwater is available as a groundwater resource (approximate renewal period of over a 1,000 years).
-Very little freshwater budget is available as surface water (lakes, rivers), or as groundwater that is recharged over a short duration.
Learning Goals: 1.2, 1.7

## Slide 13
Water use
13
Notes: 13

## Slide 14: Water footprint for products
Water input to each stage in the product life cycle
+ water required to dilute pollutants
= water footprint
materials, energy, water
waste, heat, toxins
Notes: A.Y. Hokestra and A.K. Chapagain., Water footprints of nations: Water use by peoples as a function of their consumption pattern, Water Resource Manage, 2006.
R. Dominguez-Faus, et al., The Water Footprint of Biofuels: A Drink or Drive Issue, Environmental Science and Technology, 2009, vol 43, pp 3005-3010.
Information on the water footprint can be found on pp. 358-360, J.R. Mihelcic and J.B. Zimmerman (Environmental Engineering: Fundamentals, Sustainability, Design, John Wiley & Sons, Inc., 2010).
Learning Goals: 1.8, 1.9, 1.10,

## Slide 15: Consumption defined
Consumptive water use
evaporated, transpired, incorporated into products or crops, consumed by humans or livestock, or otherwise removed from an immediate water environment
Classroom Activity (10-20 minutes)
Make a schematic sketch of the hydrological cycle. Indicate where in the cycle that there is “non-consumptive” uses of water and consumptive uses of water?
Suggest how consumptive uses can be converted to non-consumptive uses.
Consumptive-use coefficient
Notes: Further information concerning consumptive water use may be found by referencing: http://pubs.usgs.gov/fs/2008/3032/pdf/fs2008-3032.pdf
This USGS study is a compilation of consumptive water use coefficients for the Great Lakes Basin. It was developed to improve the Great Lakes State Agencies’ understanding of consumptive water use. “Consumptive-Use Coefficients are calculated by dividing the amount of water removed from the environment and not returned (consumptive use) by the total amount of water withdrawn. Consumptive-use coefficients are normally reported as a percentage.”
Learning Goals: 1.1, 1.2, 1.6

## Slide 16: Water Withdrawal vs. Consumption
Classroom Activity (5-10 minutes)
What do you conclude from this data?
Notes: The figures show representative data of the water use in the United States, both water withdrawal and water consumption. The pieces of the pie chart stand for the percentage by which thermo-electric power (Water for Energy), irrigation and livestock use (Agriculture), industrial and mining (Industrial), and domestic and commercial (Residential) water uses account for the major components of the US withdrawal and consumption of water.
“Consumptive-Use Coefficients are calculated by dividing the amount of water removed from the environment and not returned (consumptive use) by the total amount of water withdrawn. Consumptive-use coefficients are normally reported as a percentage.”
Learning Goals: 1.2, 1.3, 4.1

## Slide 17: Water footprint (WF) definitions
Source of water:
WF Category:
Classroom Activity (5-10 minutes)
According to Hoekstra and Mekennon, the average US inhabitant had a WF of 2842 m3/yr, the average China inhabitant had a WF of 1071 m3/yr, and the average India inhabitant had a WF of 1089 m3/yr from 1996-2005. What do you think accounts for this difference?
Notes: Source of data:Hoekstra, A. Y., & Mekonnen, M. M. (2012). The water footprint of humanity. Proceedings of the National Academy of Sciences, 109(9), 3232–3237. doi:10.1073/pnas.1109936109.
This slide show the different categories of water within the water footprint. Agricultural production contributes 92% to the water footprint. According to the article cited, the volume and pattern of consumption and the WF per ton of product of the products consumed are the main factors determining the WF of a consumer.
Many very interesting summary graphics can be downloaded from
http://www.waterfootprint.org/?page=files/InfoGraphics
Learning Goals: 1.10, 1.7, 5.2

## Slide 18: Coffee and Tea for the Netherlands
Source: Waterfootprint.org
Notes: The above figure expresses the amount of “virtual water” imported to the Netherlands from the shaded countries with respect to their exportation of coffee and tea. Since each of these commodities (coffee and tea) comes from a water intensive life cycle, they are considered as indicators to the country’s gross virtual water export. The overarching theme here is to demonstrate the water intensity of these agricultural exports and to bring to light the effects of consumption patterns on the environment, near and far.
“All together, the world population requires about 110 billion cubic metres of water per year in order to be able to drink coffee.”
The source web site can be further referenced for additional data: http://www.waterfootprint.org/?page=files/CoffeeTea
Learning Goals: 1.8, 1.9

## Slide 19: Water consumption: electricity
Notes: This graphic illustrates that delivering energy, be it renewable or otherwise, requires other resources, such as water. In the schematic, the extraction, transformation and delivery stages all use water. The graphic show how much water for the different types of energy.
Learning Goals: 1.8

## Slide 20: Water consumption: electricity
Notes: This data describes the amount of water consumption for each phase (raw materials, transformation, and delivery to customer) for the different forms of energy sources.
Unlike liquid and gaseous fuels, the majority of water use in electricity occurs at the transformation stage.
Raw materials: water is consumed in order to initially harness the above energies
Transformation: during this step, water is consumed to convert the energies which were harnessed during the raw materials stage into appropriate forms for customer consumption.
"Energy Vision Update 2009 Thirsty Energy: Water and Energy in the 21st Century" from US Department of Energy, Energy Demand on Water Resources, Report to Congress on the Interdependence of Energy and Water, December 2006.
Learning Goals: 1.8, 5.3

## Slide 21: Water consumption: fuels
Class Activity
(5 minutes)
What conclusions do you draw from this data set?
What questions does this data bring up?
Notes: The schematic above shows the quantity of water withdrawn in order to deliver/produce different nonrenewable and renewable energy sources for human consumption. Pay special attention to the amount of water required for the raw materials aspect of biofuels as compared to other sources. When less water is used, the process is less energy intensive.
Raw materials: during this step, water is withdrawn to actually capture the material from its natural state
Transformation: here, water is used to convert the resources from one state into another which may be useful to consumers
"Energy Vision Update 2009 Thirsty Energy: Water and Energy in the 21st Century" from US Department of Energy, Energy Demand on Water Resources, Report to Congress on the Interdependence of Energy and Water, December 2006.
Learning Goals: 1.8, 5.3

## Slide 22
Water treatment
22
Notes: 22

## Slide 23: Treatment process
Notes: This graphic illustrates the general steps of water purification and their purpose. The inorganics and organics are only able to be removed through membrane filtration processes, such as reverse osmosis.
Learning Goals: 2.2, 2.3

## Slide 24: Industrial era methods
Water treatment in the United States
Classroom Activity (5-10 minutes)
What is of a greater concern, water consumption or energy consumption? Why? Can the energy for pumping be reduce? How?
Notes: There is not a “correct” answer for this question. Some may notice that life is dependent upon water, whereas energy is both abundant and used for economic activities. Note that in using industrial era methods of water treatment and sanitation, the water and energy consumption are intimately linked, as indicated in the data in the slide.
In terms of reducing energy for pumping, it is possible to 1. Improve the efficiency of the pumps; 2. Change the type of energy used to renewable; 3. Redesign city systems and locate cities in areas where pumping demands are less. (These are not simple, easy to implement solutions).
The amount of energy needed for pumping is related to the geography--the more varied the terrain (inclines vs. flatlands) the more energy required in pumping.
Information on water use and energy can be found on pp. 454, 502, and 511-513 from J.R. Mihelcic and J.B. Zimmerman (Environmental Engineering: Fundamentals, Sustainability, Design, John Wiley & Sons, Inc., 2010).
Learning Goals: 1.8, 5.3

## Slide 25: Developing world: point-of-use methods
Filtration through fabric
Pathogens remain
Personal filters
Removes guinea worm
Notes: Figure 18-9. Filtration through overlaid layers of fabric cloth or nylon mesh filters can remove larger size particles.
These filters using cloth or mesh can help to reduce turbidity and larger pathogens, however, generally speaking, other viruses and bacteria can still pass through. Cloth folded 4-8 times can provide a mesh size of 20um, but increases if the cloth is older or worn to only 100-150 um.
(B) Figure 18-10. Personal filters used to remove guinea worm.
The personal filtering devices prevent the parasite (Dracunculus medinensis) that causes Guinea Worm Disease from passing through the filter, and combined with proper use and education, can help to stop transmission of the pathogen and eventually eradicate the disease in the human population.
These personal filters should have a pore size of 0.15mm, and can remove particles greater than or equal to 15um.
Figures 18-9 and 18-10 were used with permission of Linda D. Phillips and can be found on page 352, Mihelcic, J. R., Fry, L.M., Myre, E.A, Phillips, L.D., & Barkdoll, B.D. (Field Guide to Environmental Engineering for Development Workers: Water, Sanitation, and Indoor Air, ASCE Press, 2009).
Web Activity: The World Health Organization’s website provides detailed information on Guinea Worm. Go to the following link (http://www.who.int/features/factfiles/guinea_worm/en/), and click on “Read more about guinea-worm disease.” You will find 10 factors on guinea-worm.
How does this point of use treatment technology work, and how does it help to prevent infection with guinea-worm?
Learning Goals: 2.3, 5.2, 5.3

## Slide 26: Hierarchy of Water Needs
Chart: Hierarchy of Water Needs
Drinking | 10
Cooking / Personal Washing | 10
Washing Clothes | 10
Cleaning Home | 10
Growing Food (Domestic Use) | 10
Waste Disposal (Sanitation) | 10
Business / Gardens / Recreation | 10
Long term- Lasting Solution
Medium term-Maintaining
Short term-Survival
Notes: Basic water requirements are met first at the base of the figure, and as more water is available, more needs are met further up on the figure. Additionally, water quality is more important at the bottom of the figure than at the base.
This figure was adapted from Figure 1. Hierarchy of water requirements from the following source:
World Health Organization (2005). Minimum water quantity needed for domestic use in emergencies. Technical Notes for Emergencies. World Health Organization. Geneva, World Health Organization,. 9. Retrieved from http://www.searo.who.int/LinkFiles/List_of_Guidelines_for_Health_Emergency_Minimum_water_quantity.pdf
Learning Goals: 3.4, 5.2