## Slide 1
Enhanced Presentation of Tomographic Data
Carmen Watts Clayton1, Bernice Mills2, George Buffleben2, Thien Vu-Nguyen3
1STAR, California State University Monterey Bay, 2Sandia National Laboratories, Livermore, CA, 3STAR, Templeton High School, Templeton, CA
Objectives
Develop ways to present the wealth of visual data created with x-ray tomography by using commercially available software to:
Simultaneously present full-view pictures of a sample with an area-of-interest in 2D stills and 3D movies.
Combine multiple movies to run simultaneously.
Abstract
X-ray tomography yields a very large amount of data in three dimensions. Effectively displaying this data to a broad audience is a challenge. Techniques are discussed to improve the presentation of movies of both 2D and 3D tomographic data using commercially available software.
Background
Materials can now be viewed non-destructively with x-rays by tomography, a technique for reconstructing 2D images of an object taken at many angles (usually covering 360 degrees) into a 3D data set. The data can then be rendered into 2D or 3D still images or movies.
Right and Below:
A metal-loaded o-ring seen
as a 2D slice (1 of 1000)
from a high magnification
movie of the interior (Right)
and a frame from a 3D
movie rendering of the
exterior of the whole part
(Below).
Because of the wealth of data created with this technique, effective ways to present the results to audiences are required. One way would be to simultaneously present two or more movies of an entire sample and an area-of-interest.
3D movies present an aspect of the object and rotating it for viewing from various angles.
Methods
Three kinds of software are used during this project:
Programs that come with the tomographic equipment are required to reconstruct the 2D images taken at a number of angles into a 3D data set. They are also used to produce both still images and movies from the data sets.
IGOR can be used to manipulate large files such as movies. To process multiple images automatically, user programming is required.
iMovie is a user-friendly presentation tool which includes Picture-In-Picture movie viewing, slide shows, and visual enhancements such as scales. It requires QuickTime reader or conversion for some presentation formats.
Conclusions
Pros and cons of each application were identified.
Attention must be paid to readability, scales, distortion, and file types when converting across platforms.
iMovie
Has user-friendly features including an intuitive interface.
Handles all file types but requires QuickTime reader or conversion application to be read by other applications or on other platforms.
Operates using iOS or Windows.
Can combine two movies to run simultaneously by using the ‘Picture-In-Picture’ feature.
IGOR
Has data-friendly functions which requires user programming skills to optimize.
Handles most file types.
Operates in iOS or Windows
Zeiss/Xradia
Is required to process raw images into 3D data sets and to render those sets into 2D and 3D slices and movies.
Produces limited file types.
Generates false color stills and movies.
Operates in Windows using a very high end computer with 40 processors.
.
    This material is based upon work supported by the Sandia National Laboratories, and S.D. Bechtel, Jr. Foundation. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the funders.
    The STAR program is administered by the Cal Poly Center for Excellence in STEM Education (CESAME) on behalf of the California State University.
Sandia National Laboratories is a multi-program laboratory managed and operated by Sandia Corporation, a wholly owned subsidiary of Lockheed Martin
Corporation, for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-AC04-94AL85000. SAND2015-6397 C
ACKNOWLEDGEMENTS
The work was acquired during a nine week period and was funded in part by STAR (STEM Teacher and Researcher Program). An appreciation is given to Dr. Bernice Mills for her encouragement, advice, and support throughout the project.
Diagram of the x-ray tomography geometry.
Three orthogonal views and one 3D false color view of a braze connecting a stainless steel inner tube with an outer cylinder.
Higher resolution scan of a portion of the same braze seen above, showing false color options and orthogonal views.
S.T.A.R. Fellow C. Watts Clayton with Zeiss/ Xradia 520 Versa x-ray computed tomography instrument.
3D rendering of the interior (rough) and exterior (smooth) of a stainless steel tube with insets for areas of interest.
iMovie rendering using Picture in Picture dual view of 2D and 3D movies of a stack of copper mesh seen at left.
Future Directions
Exhibit more than two movies together.
Create accurate post-production scales on 2D slides.
This project has been made possible with support from Chevron. www.chevron.com
Notes: 20150523 0817 A082b 4up 50 31601 61601 SVRT hue... And 20150524 1347 A082f 4up 50 37281 5358 VRT Fade80.jpg (image 4up, left top)and 20150523 A082b 4up 50 31601 61601 SVRT hueRamp sawTooth90.jpg
20150402 1527 A063b 3D 50 43576 35222 parallel cro... (image 5-in-1 cropped in IGOR using this file; left middle)
Imported graphic by Bernice, unknown source (left column, bottom)
20150524 1347 A082f 3D 37281 5358 Fade75 glow.JPG 20150524 1347 A082f 3D 37281 5358 Fade75 hueRam... 20150524 1347 A082f 3D 37281 5358 Fade75 tempera...
(Center column images cropped from above files)
Right column images from top:
iMovie P-I-P assembled from file# 20150730 0849 A047a 15 80 50 10 300 600 crop 6762 53530 movie
Center images: 20150403 0659 A056a 3and1 25 22055 13863 VRT FadeLeft.jpg; and, 20150407 A056d 4up 50 18274 23945.jpg
Lower Center images:copper mesh close up 4up 100 32691 65381 VTR.jpg; and, flase colorized interior of Oring;
Lower Image: Oring close up; 20150506 0747 A075a 3D SSD ThresholdMid.jpg; 20150407 1100 A056d_recon_Export Frame 0952 with scale 6666 25000 BlackBodyID.jpg; and, A056b recon ExportFrame 0996 5000 20000 gray blackbody.tif
Bottom image: 20150506 0747 A075a #d SSD ThresholdMid.jpg
1